RTCD297  SERIES　　　（ 105℃ 8000H）

- Compliant to the RoHS directive.

- 105℃ 8000H long life and high ripple current series.

- Used in professional power supplies and frequency converters etc.

■Specification

| Item | Performance Characteristics |
| --- | --- |
| Operating range | -25℃～+105℃ |
| Rated voltage range | 160V～450V |
| Capacitance tolerance | ±20% (20℃, 120Hz) |
| Leakage current | I≤0.01CV(μA) or1.5mA (Whichever is smaller) (20℃, after 5 minutes) C=Nominal capacitance(μF), V=Rated voltage(V) |
| Dissipation factor (20℃，120Hz) | UR(V) 160-400V 25 420,450V tanδ 0.15 0.45 0.20 |
| Stability at Low Temperature (Impedance ratio at120Hz) | UR(V) 160-400V 420,450V Z(-25℃)/Z(+20℃) 4 8 |
| Load Life | After applying rated voltage with specified ripple current for 8000 hours at 105℃(the peak voltage shall not exceed the rated voltage), and then restored for 24 hours, capacitor shall meet the following requirement: Capacitance change Within ±20% of the initial value. Dissipation factor Not more than 250% of the initial specified value. Leakage current Not more than the initial specified value. |
| Shelf Life | After storing for 1000 hours at 105℃,UR to be applied for 30 minutes and then restored for 24 hours, capacitor shall meet the following requirement: Capacitance change Within ±20% of the initial value. Dissipation factor Not more than 250% of the initial specified value. Leakage current Not more than the initial specified value. |
| Standard | JIS C 5101-4 |

■Coefficient of rated ripple current

| 温度(℃) | 40 | 55 | 70 | 85 | 105 |  | 频率(Hz) UR(V) | 50(60) | 120 | 300 | 1K | ≥10K |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 系数 | 2.7 | 2.5 | 2.1 | 1.7 | 1.0 |  | 160-250 | 0.81 | 1.00 | 1.17 | 1.2 | 1.50 |
|  |  |  |  |  |  |  | 350-450 | 0.77 | 1.00 | 1.16 | 1.41 | 1.43 |

■Drawing                                Unit：mm

*:Shorter terminal is: 4.0±0.5mm

■RTCD297 Dimensions

| Rated Voltage code (V.DC) | Capacitance ( μF) | Case size ΦD×L(mm) | tanδ 20℃, 120Hz | Ripple current 105℃, 120Hz (Arms) | Part number |
| --- | --- | --- | --- | --- | --- |
| 160 2C (200) | 330 | 22×25 | 0.15 | 1.11 | RTCD2972C331KP025M |
|  | 390 | 22×30 | 0.15 | 1.26 | RTCD2972C391KP030M |
|  | 470 | 22×30 | 0.15 | 1.39 | RTCD2972C471KP030M |
|  |  | 25×25 | 0.15 | 1.38 | RTCD2972C471YQ025M |
|  | 560 | 22x35 | 0.15 | 1.55 | RTCD2972C561KP035M |
|  |  | 25x30 | 0.15 | 1.55 | RTCD2972C561KQ030M |
|  | 680 | 22x40 | 0.15 | 1.75 | RTCD2972C681KP040M |
|  |  | 25x35 | 0.15 | 1.78 | RTCD2972C681KQ035M |
|  |  | 30x25 | 0.15 | 1.74 | RTCD2972C681KR025M |
|  | 820 | 22x50 | 0.15 | 1.97 | RTCD2972C821KP050M |
|  |  | 25x40 | 0.15 | 2.01 | RTCD2972C821KQ040M |
|  |  | 30x30 | 0.15 | 1.96 | RTCD2972C821KR030M |
|  | 1000 | 25x45 | 0.15 | 2.27 | RTCD2972C102KQ045M |
|  |  | 30x35 | 0.15 | 2.26 | RTCD2972C102KR035M |
|  | 1200 | 25x50 | 0.15 | 2.54 | RTCD2972C122KQ050M |
|  |  | 30x40 | 0.15 | 2.56 | RTCD2972C122KQ040M |
|  |  | 35x30 | 0.15 | 2.52 | RTCD2972C122KS030M |
|  | 1500 | 30x45 | 0.15 | 2.96 | RTCD2972C152KR045M |
|  |  | 35x35 | 0.15 | 2.89 | RTCD2972C152KS035M |
|  | 1800 | 30x50 | 0.15 | 3.32 | RTCD2972C182KR050M |
|  |  | 35x40 | 0.15 | 3.30 | RTCD2972C182KS040M |
|  | 2200 | 35x50 | 0.15 | 3.87 | RTCD2972C222KS050M |
| 180 2K (225) | 270 | 22×25 | 0.15 | 1.00 | RTCD2972K271KP025M |
|  | 330 | 22×30 | 0.15 | 1.16 | RTCD2972K331KP030M |
|  | 390 | 22×30 | 0.15 | 1.26 | RTCD2972K391KP030M |
|  |  | 25×25 | 0.15 | 1.26 | RTCD2972K391KQ025M |
|  | 470 | 22X35 | 0.15 | 1.42 | RTCD2972K471KP035M |
|  |  | 25X30 | 0.15 | 1.42 | RTCD2972K471KQ030M |
|  | 560 | 22X40 | 0.15 | 1.59 | RTCD2972K561KP040M |
|  |  | 25X30 | 0.15 | 1.55 | RTCD2972K561KQ030M |
|  |  | 30X25 | 0.15 | 1.58 | RTCD2972K561KR025M |
|  | 680 | 22X45 | 0.15 | 1.79 | RTCD2972K681KP045M |
|  |  | 25X35 | 0.15 | 1.78 | RTCD2972K681KQ035M |
|  |  | 30X30 | 0.15 | 1.79 | RTCD2972K681KR030M |
|  | 820 | 25X40 | 0.15 | 2.01 | RTCD2972K821KQ040M |
|  |  | 30X35 | 0.15 | 2.04 | RTCD2972K821KR035M |
|  | 1000 | 25X50 | 0.15 | 2.32 | RTCD2972K102KP050M |
|  |  | 30X35 | 0.15 | 2.26 | RTCD2972K102KR035M |
|  |  | 35X30 | 0.15 | 2.30 | RTCD2972K102KS030M |
|  | 1200 | 30X45 | 0.15 | 2.65 | RTCD2972K122KR045M |
|  |  | 35X35 | 0.15 | 2.58 | RTCD2972K122KS035M |
|  | 1500 | 30X50 | 0.15 | 3.03 | RTCD2972K152KR050M |
|  |  | 35X40 | 0.15 | 3.01 | RTCD2972K152KS040M |
|  | 1800 | 35X45 | 0.15 | 3.41 | RTCD2972K182KS045M |
|  | 2200 | 35X50 | 0.15 | 3.87 | RTCD2972K222KS050M |
| 200 2D (250) | 220 | 22X25 | 0.15 | 0.90 | RTCD2972D221KP025M |
|  | 270 | 22X30 | 0.15 | 1.05 | RTCD2972D271KP030M |
|  | 330 | 22X30 | 0.15 | 1.16 | RTCD2972D331KP030M |
|  |  | 25X25 | 0.15 | 1.16 | RTCD2972D331KQ025M |
|  | 390 | 22X35 | 0.15 | 1.29 | RTCD2972D391KP035M |
|  |  | 25X30 | 0.15 | 1.29 | RTCD2972D391KQ030M |
|  | 470 | 22X40 | 0.15 | 1.46 | RTCD2972D471KP040M |
|  |  | 25X30 | 0.15 | 1.42 | RTCD2972D471KQ030M |
|  |  | 30X25 | 0.15 | 1.45 | RTCD2972D471KR025M |
|  | 560 | 22X45 | 0.15 | 1.63 | RTCD2972D561KP045M |
|  |  | 25X35 | 0.15 | 1.62 | RTCD2972D561KQ035M |
|  |  | 30X30 | 0.15 | 1.62 | RTCD2972D561KR030M |
|  | 680 | 25X40 | 0.15 | 1.83 | RTCD2972D681KQ040M |
|  |  | 30X30 | 0.15 | 1.79 | RTCD2972D681KR030M |
|  | 820 | 25X45 | 0.15 | 2.06 | RTCD2972D821KQ045M |
|  |  | 30X35 | 0.15 | 2.04 | RTCD2972D821KR035M |
|  | 1000 | 30X45 | 0.15 | 2.42 | RTCD2972D102KQ045M |
|  |  | 35X30 | 0.15 | 2.30 | RTCD2972D102KS030M |
|  | 1200 | 30X50 | 0.15 | 2.71 | RTCD2972D122KR050M |

| Rated Voltage code (V.DC) | Capacitance ( μF) | Case size ΦD×L(mm) | tanδ 20℃, 120Hz | Ripple current 105℃, 120Hz (Arms) | Part number |
| --- | --- | --- | --- | --- | --- |
| 200 2D (250) | 1200 | 35X40 | 0.15 | 2.70 | RTCD2972D122KS040M |
|  | 1500 | 35X45 | 0.15 | 3.11 | RTCD2972D152KS045M |
|  | 1800 | 35X50 | 0.15 | 3.50 | RTCD2972D182KS050M |
| 250 2E (300) | 180 | 22X25 | 0.15 | 0.82 | RTCD2972E181KP025M |
|  | 220 | 22X30 | 0.15 | 0.95 | RTCD2972E221KP030M |
|  | 270 | 22X35 | 0.15 | 1.08 | RTCD2972E271KP035M |
|  |  | 25X25 | 0.15 | 1.05 | RTCD2972E271KQ025M |
|  | 330 | 22X40 | 0.15 | 1.22 | RTCD2972E331KP040M |
|  |  | 25X30 | 0.15 | 1.19 | RTCD2972E331KQ030M |
|  | 390 | 22X45 | 0.15 | 1.36 | RTCD2972E391KP045M |
|  |  | 25X35 | 0.15 | 1.35 | RTCD2972E391KQ035M |
|  |  | 30X25 | 0.15 | 1.32 | RTCD2972E391KR025M |
|  | 470 | 22X50 | 0.15 | 1.49 | RTCD2972E471KP050M |
|  |  | 25X40 | 0.15 | 1.52 | RTCD2972E471KQ040M |
|  |  | 30X30 | 0.15 | 1.49 | RTCD2972E471KR030M |
|  | 560 | 25X45 | 0.15 | 1.70 | RTCD2972E561KQ045M |
|  |  | 30X35 | 0.15 | 1.69 | RTCD2972E561KR035M |
|  | 680 | 25X50 | 0.15 | 1.91 | RTCD2972E681KQ050M |
|  |  | 30X40 | 0.15 | 1.93 | RTCD2972E681KR040M |
|  |  | 35X30 | 0.15 | 1.90 | RTCD2972E681KS030M |
|  | 820 | 30X45 | 0.15 | 2.19 | RTCD2972E821KR045M |
|  |  | 35X35 | 0.15 | 2.13 | RTCD2972E821KS035M |
|  | 1000 | 35X40 | 0.15 | 2.46 | RTCD2972E102KS040M |
|  | 1200 | 35X50 | 0.15 | 2.86 | RTCD2972E122KS050M |
| 350 2V (400) | 100 | 22X25 | 0.15 | 0.67 | RTCD2972V101KP025M |
|  | 120 | 22X30 | 0.15 | 0.77 | RTCD2972V121KP030M |
|  |  | 25X25 | 0.15 | 0.76 | RTCD2972V121KQ025M |
|  | 150 | 22X35 | 0.15 | 0.88 | RTCD2972V151KP035M |
|  |  | 25X30 | 0.15 | 0.88 | RTCD2972V151KQ030M |
|  | 180 | 22X40 | 0.15 | 0.99 | RTCD2972V181KP040M |
|  |  | 25X30 | 0.15 | 0.96 | RTCD2972V181KQ030M |
|  |  | 30X25 | 0.15 | 0.98 | RTCD2972V181KR025M |
|  | 220 | 22X45 | 0.15 | 1.12 | RTCD2972V221KP045M |
|  |  | 25X35 | 0.15 | 1.11 | RTCD2972V221KQ035M |
|  |  | 30X30 | 0.15 | 1.11 | RTCD2972V221KR030M |
|  | 270 | 25X40 | 0.15 | 1.26 | RTCD2972V271KQ040M |
|  |  | 30X35 | 0.15 | 1.28 | RTCD2972V271KR035M |
|  | 330 | 25X45 | 0.15 | 1.40 | RTCD2972V331KQ045M |
|  |  | 30X35 | 0.15 | 1.42 | RTCD2972V331KR035M |
|  |  | 35X30 | 0.15 | 1.45 | RTCD2972V331KS030M |
|  | 390 | 30X40 | 0.15 | 1.60 | RTCD2972V391KR040M |
|  |  | 35X35 | 0.15 | 1.61 | RTCD2972V391KS035M |
|  | 470 | 30X50 | 0.15 | 1.86 | RTCD2972V471KR050M |
|  |  | 35X40 | 0.15 | 1.85 | RTCD2972V471KS040M |
|  | 560 | 35X40 | 0.15 | 2.02 | RTCD2972V561KS040M |
|  | 680 | 35X50 | 0.15 | 2.36 | RTCD2972V681KS050M |
| 400 2G (450) | 68 | 22X25 | 0.15 | 0.55 | RTCD2972G680KP025M |
|  | 82 | 22X30 | 0.15 | 0.63 | RTCD2972G820KP030M |
|  | 100 | 22X30 | 0.15 | 0.70 | RTCD2972G101KP030M |
|  |  | 25X25 | 0.15 | 0.70 | RTCD2972G101KQ025M |
|  | 120 | 22X35 | 0.15 | 0.79 | RTCD2972G121KP035M |
|  |  | 25X30 | 0.15 | 0.79 | RTCD2972G121KQ030M |
|  | 150 | 22X40 | 0.15 | 0.90 | RTCD2972G151KP040M |

| Rated Voltage code (V.DC) | Capacitance ( μF) | Case size ΦD×L(mm) | tanδ 20℃, 120Hz | Ripple curre0.88nt 105℃, 120Hz (Arms) | Part number |
| --- | --- | --- | --- | --- | --- |
| 400 2G (450) | 150 | 25X30 | 0.15 | 0.88 | RTCD2972G151KQ030M |
|  |  | 30X25 | 0.15 | 0.90 | RTCD2972G151KR025M |
|  | 180 | 22X45 | 0.15 | 0.99 | RTCD2972G181KP045M |
|  |  | 25X35 | 0.15 | 1.01 | RTCD2972G181KQ035M |
|  |  | 30X30 | 0.15 | 1.01 | RTCD2972G181KR030M |
|  | 220 | 25X40 | 0.15 | 1.14 | RTCD2972G221KQ040M |
|  |  | 30X35 | 0.15 | 1.16 | RTCD2972G221KR035M |
|  | 270 | 25X50 | 0.15 | 1.32 | RTCD2972G271KQ050M |
|  |  | 30X40 | 0.15 | 1.33 | RTCD2972G271KR040M |
|  |  | 35X30 | 0.15 | 1.31 | RTCD2972G271KS030M |
|  | 330 | 30X45 | 0.15 | 1.52 | RTCD2972G331KR045M |
|  |  | 35X35 | 0.15 | 1.48 | RTCD2972G331KS035M |
|  | 390 | 30X50 | 0.15 | 1.69 | RTCD2972G391KR050M |
|  |  | 35X40 | 0.15 | 1.68 | RTCD2972G391KS040M |
|  | 470 | 35X45 | 0.15 | 1.91 | RTCD2972G471KS045M |
|  | 560 | 35X50 | 0.15 | 2.14 | RTCD2972G561KS050M |
| 450 2W (500) | 47 | 22X25 | 0.20 | 0.46 | RTCD2972W470KP025M |
|  | 56 | 22X30 | 0.20 | 0.52 | RTCD2972W560KP030M |
|  | 68 | 22X30 | 0.20 | 0.58 | RTCD2972W680KP030M |
|  |  | 25X25 | 0.20 | 0.58 | RTCD2972W680KQ025M |
|  | 82 | 22X35 | 0.20 | 0.65 | RTCD2972W820KP035M |
|  |  | 25X30 | 0.20 | 0.65 | RTCD2972W820KQ030M |
|  | 100 | 22X40 | 0.20 | 0.74 | RTCD2972W101KP040M |
|  |  | 25X30 | 0.20 | 0.72 | RTCD2972W101KQ030M |
|  |  | 30X25 | 0.20 | 0.73 | RTCD2972W101KR025M |
|  | 120 | 22X45 | 0.20 | 0.83 | RTCD2972W121KP045M |
|  |  | 25X35 | 0.20 | 0.82 | RTCD2972W121KQ035M |
|  |  | 30X30 | 0.20 | 0.82 | RTCD2972W121KR030M |
|  | 150 | 25X40 | 0.20 | 0.94 | RTCD2972W151KQ040M |
|  |  | 30X35 | 0.20 | 0.96 | RTCD2972W151KR035M |
|  | 180 | 25X45 | 0.20 | 1.06 | RTCD2972W181KQ045M |
|  |  | 30X35 | 0.20 | 1.05 | RTCD2972W181KR035M |
|  |  | 35X30 | 0.20 | 1.07 | RTCD2972W181KS030M |
|  | 220 | 30X40 | 0.20 | 1.20 | RTCD2972W221KR040M |
|  |  | 35X35 | 0.20 | 1.21 | RTCD2972W221KS035M |
|  | 270 | 30X50 | 0.20 | 1.41 | RTCD2972W271KR050M |
|  |  | 35X40 | 0.20 | 1.40 | RTCD2972W271KS040M |
|  | 330 | 35X45 | 0.20 | 1.60 | RTCD2972W331KS045M |
|  | 390 | 35X50 | 0.20 | 1.79 | RTCD2972W391KS050M |