RTCD138  SERIES　（105℃ 5000H）

●Compliant to the RoHS directive.

●Leading product with heat resistance and long life at 105℃ to meet

the requirement for high temperature and long life in the inverter circuit.

■Product Specifications

| (unit: mm) | Items | Specifications |
| --- | --- | --- |
|  | Temperature range | -40℃～+105℃ |
|  | Rated voltage | 350～550V.DC |
|  | Capacitance tolerance | ±20% (20℃, 120Hz) |
|  | Leakage current | 0.01CV (μA) or 5 mA,whichever is smaller or less |
|  |  | [ C=nominal capacitance (μF),V= rated voltage (V) ] |
|  | Dissipation factor | Less than the value specified in the standard products table. |
|  | Permissible ripple current | As specified in the standard products table. (105℃, 120Hz) |
|  | High-temperature load | After the rated voltage with specified ripple current is applied at 105℃ for 5000 hours : Capacitance tolerance : ±20% or less of the initial value Dissipation factor : 200% or less of the specified initial value Leakage current : Specified initial value or less |
| ΦD | P | S | T | Cap material |  |  |  |
| 51 | 22.0 | M5×10 | 5.5 | Phenol |  |  |  |
| 64 | 28.6 | M5×10 | 5.5 | Phenol |  |  |  |
| 77 | 32.0 | M5×10 | 4.5 | Phenol |  |  |  |
| 90 | 32.0 | M5×10 | 4.0 | Phenol |  | standard | JIS C 5101-4 |

| Ripple current correction coefficient |  | Part number(Example): RTCD138 400V 10,000μF±20% F case（Φ90mm）product |
| --- | --- | --- |
| Temperature (℃) | 40 | 60 | 85 | 105 |  |  | RTCD138 2G 103 Y F 196 M D 5 Series Voltage Code Capacitance code Mounting style Diameter code Length Cap. tolerance Diameter Terminal Type of screw |
| Coefficient | 2.44 | 2.16 | 2.0 | 1.0 |  |  |  |
| Frequency (Hz) | 50/60 | 120 | 300 | 1K | ≥10K |  |  |
| Coefficient | 0.7 | 1.0 | 1.1 | 1.3 | 1.4 |  |  |

■Standard Products Table

| Rated Voltage Code (V.DC) | Capacitance (μF) | Case size ΦD×L(mm) | tanδ 20℃, 120Hz | Ripple current 105℃, 120Hz (Arms) | ESR(typ.) 20℃, 100Hz (mΩ) | Z max 20℃, 10KHz (mΩ) | Part number |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 350 2V (400) | 1000 | 51×75 | 0.15 | 3.9 | 100 | 103 | RTCD1382V102YC075M |
|  | 1200 | 51×75 | 0.15 | 4.2 | 84 | 87 | RTCD1382V122YC075M |
|  | 1500 | 51×96 | 0.15 | 5.2 | 67 | 69 | RTCD1382V152YC096M |
|  | 1800 | 51×96 | 0.15 | 5.7 | 55 | 57 | RTCD1382V182YC096M |
|  | 2200 | 51×130 | 0.15 | 7.1 | 45 | 47 | RTCD1382V222YC130M |
|  | 2700 | 64×96 | 0.15 | 7.7 | 37 | 39 | RTCD1382V272YD096M |
|  | 3300 | 64×115 | 0.15 | 9.1 | 29 | 31 | RTCD1382V332YD115M |
|  | 3900 | 64×130 | 0.15 | 10.4 | 25 | 27 | RTCD1382V392YD130M |
|  | 4700 | 64×155 | 0.15 | 12.2 | 20 | 21 | RTCD1382V472YD155M |
|  |  | 77×115 | 0.15 | 11.5 | 20 | 21 | RTCD1382V472YE115M |
|  | 5600 | 64×195 | 0.15 | 14.6 | 17 | 20 | RTCD1382V562YD195M |
|  |  | 77×130 | 0.15 | 13.1 | 17 | 20 | RTCD1382V562YE130M |
|  | 6800 | 77×155 | 0.15 | 15.5 | 14 | 18 | RTCD1382V682YE155M |
|  | 8200 | 90×157 | 0.15 | 18.1 | 12 | 15 | RTCD1382V822YF157M |
|  | 10000 | 90×157 | 0.15 | 19.9 | 10 | 15 | RTCD1382V103YF157M |
|  | 12000 | 90×196 | 0.15 | 23.8 | 8 | 13 | RTCD1382V123YF196M |
|  | 15000 | 90×236 | 0.15 | 28.8 | 7 | 10 | RTCD1382V153YF236M |

| Rated Voltage Code (V.DC) | Capacitance (μF) | Case size ΦD×L(mm) | tanδ 20℃, 120Hz | Ripple current 105℃, 120Hz (Arms) | ESR(typ.) 20℃, 100Hz (mΩ) | Z max 20℃, 10KHz (mΩ) | Part number |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 400 2G (450) | 1000 | 51×75 | 0.15 | 3.9 | 102 | 105 | RTCD1382G102YC075M |
|  | 1200 | 51×96 | 0.15 | 4.6 | 85 | 88 | RTCD1382G122YC096M |
|  | 1500 | 51×115 | 0.15 | 5.6 | 68 | 70 | RTCD1382G152YC115M |
|  | 1800 | 51×130 | 0.15 | 6.4 | 57 | 58 | RTCD1382G182YC130M |
|  | 2200 | 64×96 | 0.15 | 6.9 | 46 | 48 | RTCD1382G222YD096M |
|  | 2700 | 64×115 | 0.15 | 8.2 | 38 | 40 | RTCD1382G272YD115M |
|  | 3300 | 64×130 | 0.15 | 9.5 | 30 | 32 | RTCD1382G332YD130M |
|  | 3900 | 64×155 | 0.15 | 11.1 | 27 | 28 | RTCD1382G392YD155M |
|  |  | 77×115 | 0.15 | 10.4 | 27 | 28 | RTCD1382G392YE115M |
|  | 4700 | 64×195 | 0.15 | 13.4 | 21 | 22 | RTCD1382G472YD195M |
|  |  | 77×130 | 0.15 | 12.0 | 21 | 22 | RTCD1382G472YE130M |
|  | 5600 | 64×195 | 0.15 | 14.6 | 20 | 20 | RTCD1382G562YD195M |
|  |  | 77×155 | 0.15 | 14.0 | 20 | 20 | RTCD1382G562YE155M |
|  | 6800 | 90×157 | 0.15 | 16.5 | 18 | 18 | RTCD1382G682YF157M |
|  | 8200 | 90×157 | 0.15 | 18.1 | 15 | 17 | RTCD1382G822YF157M |
|  | 10000 | 90×196 | 0.15 | 21.7 | 12 | 15 | RTCD1382G103YF196M |
|  | 12000 | 90×236 | 0.15 | 25.8 | 10 | 12 | RTCD1382G123YF236M |
|  | 15000 | 90*236 | 0.15 | 28.0 | 10 | 12 | RTCD1382G153YF236M |
| 450 2W (500) | 1000 | 51×96 | 0.15 | 4.2 | 102 | 105 | RTCD1382W102YC096M |
|  | 1200 | 51×115 | 0.15 | 5.0 | 85 | 88 | RTCD1382W122YC115M |
|  | 1500 | 51×130 | 0.15 | 5.9 | 68 | 70 | RTCD1382W152YC130M |
|  | 1800 | 64×96 | 0.15 | 6.3 | 57 | 58 | RTCD1382W182YD096M |
|  | 2200 | 64×115 | 0.15 | 7.4 | 46 | 48 | RTCD1382W222YD115M |
|  | 2700 | 64×130 | 0.15 | 8.6 | 40 | 42 | RTCD1382W272YD130M |
|  |  | 77×115 | 0.15 | 8.7 | 40 | 42 | RTCD1382W272YE115M |
|  | 3300 | 64×155 | 0.15 | 10.2 | 30 | 35 | RTCD1382W332YD155M |
|  |  | 77×130 | 0.15 | 10.1 | 30 | 35 | RTCD1382W332YE130M |
|  | 3900 | 64×195 | 0.15 | 12.3 | 27 | 32 | RTCD1382W392YD195M |
|  | 4700 | 77×155 | 0.15 | 12.9 | 24 | 27 | RTCD1382W472YE155M |
|  | 5600 | 77×195 | 0.15 | 15.4 | 22 | 23 | RTCD1382W562YE195M |
|  |  | 90×157 | 0.15 | 14.9 | 22 | 23 | RTCD1382W562YF157M |
|  | 6800 | 90×196 | 0.15 | 18 | 20 | 20 | RTCD1382W682YF196M |
|  | 8200 | 90×196 | 0.15 | 19.8 | 18 | 18 | RTCD1382W822YF196M |
|  | 10000 | 90×196 | 0.15 | 21.6 | 15 | 15 | RTCD1382W103YF196M |
|  | 10000 | 90×236 | 0.15 | 23.6 | 15 | 15 | RTCD1382W103YF236M |
| 500 2H (550) | 1000 | 51×130 | 0.15 | 4.5 | 112 | 120 | RTCD1382H102YC130M |
|  | 1200 | 64×115 | 0.15 | 5.2 | 93 | 100 | RTCD1382H122YD115M |
|  | 1500 | 61×130 | 0.15 | 6.1 | 74 | 80 | RTCD1382H152YD130M |
|  | 1800 | 77×115 | 0.15 | 6.7 | 62 | 50 | RTCD1382H182YE115M |
|  | 2200 | 77×130 | 0.15 | 7.3 | 53 | 50 | RTCD1382H222YE130M |
|  | 2700 | 77×155 | 0.15 | 8.7 | 40 | 35 | RTCD1382H272YE155M |
|  | 3300 | 77×155 | 0.15 | 10.0 | 38 | 32 | RTCD1382H332YE155M |
|  | 3900 | 90×157 | 0.15 | 11.6 | 30 | 27 | RTCD1382H392YF157M |
|  | 4700 | 90×170 | 0.15 | 13.3 | 25 | 20 | RTCD1382H472YF170M |
|  | 5600 | 90×196 | 0.15 | 15.5 | 20 | 17 | RTCD1382H562YF196M |
|  | 6800 | 90×196 | 0.15 | 17.0 | 17 | 17 | RTCD1382H682YF196M |
|  |  | 90×236 | 0.15 | 18.5 | 17 | 17 | RTCD1382H682YF236M |
| 550 2Y (600) | 1000 | 64×115 | 0.15 | 4.8 | 110 | 115 | RTCD1382Y102YD115M |
|  | 1200 | 64×130 | 0.15 | 5.6 | 90 | 100 | RTCD1382H122YD130M |
|  | 1500 | 77×115 | 0.15 | 6.6 | 70 | 85 | RTCD1382H152YE115M |
|  | 1800 | 77×130 | 0.15 | 7.2 | 60 | 65 | RTCD1382H182YE130M |
|  | 2200 | 77×155 | 0.15 | 8.4 | 50 | 55 | RTCD1382H222YE155M |
|  | 2700 | 77×170 | 0.15 | 10.0 | 40 | 45 | RTCD1382H272YE170M |

| Rated Voltage Code (V.DC) | Capacitance (μF) | Case size ΦD×L(mm) | tanδ 20℃, 120Hz | Ripple current 105℃, 120Hz (Arms) | ESR(typ.) 20℃, 100Hz (mΩ) | Z max 20℃, 10KHz (mΩ) | Part number |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 550 2Y (600) | 3300 | 90×157 | 0.15 | 11.0 | 35 | 40 | RTCD1382H332YF157M |
|  | 3900 | 90×170 | 0.15 | 12.8 | 30 | 35 | RTCD1382H392YF170M |
|  | 4700 | 90×196 | 0.15 | 14.5 | 25 | 30 | RTCD1382H472YF196M |
|  | 5600 | 90×236 | 0.15 | 16.7 | 20 | 20 | RTCD1382H562YF236M |