RTCDT  SERIES　（85℃ 2000H）

●Compliant to the RoHS directive.

●350WV~500WV extra-high voltage.

●85℃ 2000H for inverters.

■Product Specifications

| (unit: mm) | Items | Specifications |
| --- | --- | --- |
|  | Temperature range | -25℃～+85℃ |
|  | Rated voltage | 350～500V.DC |
|  | Capacitance tolerance | ±20% (20℃, 120Hz) |
|  | Leakage current | 0.01CV (μA)or 5mA,whichever is smaller |
|  |  | [C=nominal capacitance (μF),V= rated voltage (V)] |
|  | Dissipation factor | Less than the value specified in the standard products table. |
| ΦD | P | S | T | Cap material |  | Permissible ripple current | As specified in the standard products table. (40℃, 120Hz) |
| 36 | 12.7 | M5×10 | 6.0 | Phenol |  | High-temperature load | After the rated voltage with specified ripple current is applied at 85℃ for 2,000 hours : Capacitance tolerance : ±20% or less of the initial value Dissipation factor : 200% or less of the specified initial value Leakage current : Specified initial value or less |
| 51 | 22.0 | M5×10 | 5.5 | Phenol |  |  |  |
| 64 | 28.6 | M5×10 | 5.5 | Phenol |  |  |  |
| 77 | 32.0 | M5×10 | 4.5 | Phenol |  |  |  |
| 90 | 32.0 | M5×10 | 4.0 | Phenol |  |  |  |
| 101 | 41.5 | M8×17 | 10.0 | Phenol |  | Standard | JIS C 5101-4 |

| Ripple current correction coefficient |  | Part number(Example): RTCD135 400V 10,000μF±20% F case（Φ90mm）product |
| --- | --- | --- |
| Temperature (℃) | 40 | 60 | 70 | 85 |  |  | RTCDT 2G 103 Y F 157 M D 5 Series Voltage Code Capacitance code Mounting style Diameter code Length Cap. tolerance Diameter Terminal Type of screw |
| Coefficient | 1.0 | 0.75 | 0.62 | 0.37 |  |  |  |
| Frequency (Hz) | 50/60 | 120 | 300 | 1K | ≥10K |  |  |
| Coefficient | 0.7 | 1.0 | 1.1 | 1.3 | 1.4 |  |  |

■Standard Products Table

| Rated Voltage Code (V.DC) | Capacitance (μF) | Case size ΦD×L(mm) | tanδ 20℃, 120Hz | Ripple current 40℃, 120Hz (Arms) | ESR(typ.) 20℃, 100Hz (mΩ) | Z max 20℃, 10KHz (mΩ) | Part number |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 350 2V (400) | 1200 | 51×75 | 0.15 | 10.3 | 90 | 120 | RTCDT2V122YC075M |
|  | 1500 | 51×75 | 0.15 | 11.5 | 77 | 100 | RTCDT2V152YC075M |
|  | 1800 | 51×96 | 0.15 | 13.9 | 62 | 80 | RTCDT2V182YC096M |
|  | 2200 | 51×96 | 0.15 | 15.4 | 51 | 70 | RTCDT2V222YC130M |
|  | 2700 | 51×130 | 0.15 | 19.3 | 51 | 58 | RTCDT2V272YC130M |
|  | 3300 | 51×130 | 0.15 | 21.4 | 35 | 51 | RTCDT2V332YC130M |
|  | 3900 | 64×115 | 0.15 | 24.2 | 30 | 47 | RTCDT2V392YD115M |
|  | 4700 | 64×130 | 0.15 | 27.9 | 28 | 40 | RTCDT2V472YD130M |
|  | 5600 | 77×115 | 0.15 | 30.7 | 25 | 35 | RTCDT2V562YE115M |
|  | 6800 | 77×130 | 0.15 | 35.4 | 20 | 29 | RTCDT2V682YE130M |
|  | 8200 | 77×155 | 0.15 | 41.7 | 17 | 25 | RTCDT2V822YE155M |
| Rated Voltage Code (V.DC) | Capacitance (μF) | Case size ΦD×L(mm) | tanδ 20℃, 120Hz | Ripple current 40℃, 120Hz (Arms) | ESR(typ.) 20℃, 100Hz (mΩ) | Z max 20℃, 10KHz (mΩ) | Part number |
| 350 2W (400) | 10000 | 90×157 | 0.15 | 49.0 | 15 | 23 | RTCDT2V103YF157M |
|  | 12000 | 90×157 | 0.15 | 54.1 | 13 | 21 | RTCDT2V123YF157M |
|  | 15000 | 90×196 | 0.15 | 66.2 | 10 | 20 | RTCDT2V153YF196M |
|  | 18000 | 90×220 | 0.15 | 75.4 | 8 | 20 | RTCDT2V183YF220M |
|  | 22000 | 90×236 | 0.15 | 80.9 | 8 | 20 | RTCDT2V223YF236M |
| 400 2G (450) | 1000 | 51×75 | 0.15 | 9.4 | 85 | 105 | RTCDT2G102YC075M |
|  |  | 51×100 | 0.15 | 10.6 | 85 | 150 | RTCDT2G122YC100M |
|  | 1200 | 51×80 | 0.15 | 10.3 | 75 | 125 | RTCDT2G152YC080M |
|  | 1500 | 51×96 | 0.15 | 12.7 | 62 | 108 | RTCDT2G152YC096M |
|  |  | 51×100 | 0.15 | 12.7 | 62 | 108 | RTCDT2G152YC100M |
|  | 1800 | 51×96 | 0.15 | 13.9 | 51 | 90 | RTCDT2G182YC096M |
|  |  | 64×96 | 0.15 | 15.6 | 51 | 90 | RTCDT2G182YD096M |
|  | 2200 | 51×100 | 0.15 | 16.1 | 39 | 75 | RTCDT2G222YC100M |
|  |  | 51×105 | 0.15 | 16.1 | 39 | 75 | RTCDT2G222YC105M |
|  |  | 51×115 | 0.15 | 16.1 | 39 | 75 | RTCDT2G222YC115M |
|  |  | 51×130 | 0.15 | 17.4 | 39 | 75 | RTCDT2G222YC130M |
|  |  | 64×80 | 0.15 | 16.1 | 39 | 75 | RTCDT2G222YD080M |
|  |  | 64×96 | 0.15 | 17.0 | 39 | 75 | RTCDT2G222YD096M |
|  |  | 77×90 | 0.15 | 19.0 | 39 | 75 | RTCDT2G222YE090M |
|  | 2700 | 64×96 | 0.15 | 18.8 | 36 | 66 | RTCDT2G272YD096M |
|  | 3300 | 64×96 | 0.15 | 20.5 | 35 | 53 | RTCDT2G332YD096M |
|  |  | 64×115 | 0.15 | 22.2 | 35 | 53 | RTCDT2G332YD115M |
|  |  | 77×96 | 0.15 | 22.2 | 35 | 53 | RTCDT2G332YE096M |
|  |  | 77×100 | 0.15 | 22.2 | 35 | 53 | RTCDT2G332YE100M |
|  | 3900 | 64×115 | 0.15 | 24.0 | 29 | 48 | RTCDT2G392YD115M |
|  |  | 64×130 | 0.15 | 25.0 | 29 | 48 | RTCDT2G392YD130M |
|  |  | 77×96 | 0.15 | 24.0 | 29 | 48 | RTCDT2G392YE096M |
|  | 4700 | 64×115 | 0.15 | 25.6 | 26 | 41 | RTCDT2G472YD115M |
|  |  | 64×130 | 0.15 | 25.6 | 26 | 41 | RTCDT2G472YD130M |
|  |  | 77×96 | 0.15 | 25.0 | 26 | 41 | RTCDT2G472YE096M |
|  |  | 77×105 | 0.15 | 27.1 | 26 | 41 | RTCDT2G472YE105M |
|  |  | 77×110 | 0.15 | 27.1 | 26 | 41 | RTCDT2G472YE110M |
|  |  | 77×115 | 0.15 | 28.2 | 26 | 41 | RTCDT2G472YE115M |
|  |  | 77×130 | 0.15 | 28.2 | 26 | 41 | RTCDT2G472YE130M |
|  | 5600 | 64×130 | 0.15 | 29.0 | 21 | 37 | RTCDT2G562YD130M |
|  |  | 64×155 | 0.15 | 31.0 | 21 | 37 | RTCDT2G562YD155M |
|  |  | 77×105 | 0.15 | 29.0 | 21 | 37 | RTCDT2G562YE105M |
|  |  | 77×130 | 0.15 | 32.2 | 21 | 37 | RTCDT2G562YE130M |
|  |  | 90×96 | 0.15 | 31.0 | 21 | 37 | RTCDT2G562YF096M |
|  | 5900 | 77×130 | 0.15 | 33.0 | 27 | 31 | RTCDT2G592YE130M |
|  | 6300 | 77×143 | 0.15 | 34.0 | 21 | 37 | RTCDT2G632YE143M |
|  | 6800 | 77×115 | 0.15 | 34.1 | 18 | 30 | RTCDT2G682YE115M |
|  |  | 77×130 | 0.15 | 35.0 | 18 | 30 | RTCDT2G682YE130M |
|  |  | 77×145 | 0.15 | 36.8 | 18 | 30 | RTCDT2G682YE145M |
|  |  | 77×150 | 0.15 | 36.8 | 18 | 30 | RTCDT2G682YE150M |
|  |  | 77×155 | 0.15 | 38.0 | 18 | 30 | RTCDT2G682YE155M |
|  | 8200 | 77×130 | 0.15 | 37.4 | 16 | 26 | RTCDT2G822YE130M |
|  |  | 77×145 | 0.15 | 39.2 | 16 | 26 | RTCDT2G822YE145M |
|  |  | 90×130 | 0.15 | 40.9 | 16 | 26 | RTCDT2G822YF130M |
|  |  | 90×157 | 0.15 | 44.4 | 16 | 26 | RTCDT2G822YF157M |
| Rated Voltage Code (V.DC) | Capacitance (μF) | Case size ΦD×L(mm) | tanδ 20℃, 120Hz | Ripple current 40℃, 120Hz (Arms) | ESR(typ.) 20℃, 100Hz (mΩ) | Z max 20℃, 10KHz (mΩ) | Part number |
| 400 2G (450) | 10000 | 90×130 | 0.15 | 45.5 | 13 | 23 | RTCDT2G103YF130M |
|  |  | 90×150 | 0.15 | 45.5 | 13 | 23 | RTCDT2G103YF150M |
|  |  | 90×157 | 0.15 | 49.4 | 13 | 23 | RTCDT2G103YF157M |
|  |  | 90×196 | 0.15 | 49.4 | 13 | 23 | RTCDT2G103YF196M |
|  | 12000 | 90×157 | 0.15 | 53.5 | 12 | 21 | RTCDT2G123YF157M |
|  |  | 90×196 | 0.15 | 59.1 | 12 | 21 | RTCDT2G123YF196M |
|  | 15000 | 90×220 | 0.15 | 69.1 | 11 | 21 | RTCDT2G153YF220M |
|  |  | 90×236 | 0.15 | 71.1 | 11 | 21 | RTCDT2G153YF236M |
|  | 18000 | 90×220 | 0.15 | 74.5 | 10 | 20 | RTCDT2G183YF220M |
|  |  | 90×236 | 0.15 | 76.8 | 10 | 20 | RTCDT2G183YF236M |
| 450 2G (500) | 1000 | 51×80 | 0.15 | 9.4 | 84 | 154 | RTCDT2W102YC080M |
|  | 1200 | 51×96 | 0.15 | 11.4 | 73 | 129 | RTCDT2W122YC096M |
|  | 1500 | 51×80 | 0.15 | 11.6 | 60 | 108 | RTCDT2W152YC080M |
|  |  | 51×115 | 0.15 | 13.7 | 60 | 108 | RTCDT2W152YC115M |
|  | 1800 | 51×130 | 0.15 | 15.8 | 48 | 100 | RTCDT2W182YC130M |
|  | 2200 | 51×120 | 0.15 | 16.2 | 35 | 84 | RTCDT2W222YC120M |
|  |  | 64×100 | 0.15 | 17.0 | 35 | 84 | RTCDT2W222YD100M |
|  | 2700 | 64×115 | 0.15 | 20.2 | 35 | 69 | RTCDT2W272YD115M |
|  | 3300 | 64×115 | 0.15 | 22.1 | 32 | 61 | RTCDT2W332YD115M |
|  |  | 64×130 | 0.15 | 23.4 | 32 | 61 | RTCDT2W332YD130M |
|  | 3900 | 77×115 | 0.15 | 25.6 | 32 | 51 | RTCDT2W392YE115M |
|  | 4700 | 77×115 | 0.15 | 27.8 | 26 | 43 | RTCDT2W472YE115M |
|  |  | 77×130 | 0.15 | 29.4 | 26 | 43 | RTCDT2W472YE130M |
|  | 5600 | 77×130 | 0.15 | 31.8 | 24 | 37 | RTCDT2W562YE130M |
|  |  | 77×155 | 0.15 | 34.6 | 24 | 37 | RTCDT2W562YE155M |
|  | 6800 | 77×145 | 0.15 | 35.8 | 22 | 33 | RTCDT2W682YE145M |
|  |  | 77×155 | 0.15 | 35.8 | 22 | 33 | RTCDT2W682YE155M |
|  |  | 90×130 | 0.15 | 36.9 | 22 | 33 | RTCDT2W682YF130M |
|  |  | 90×157 | 0.15 | 40.5 | 22 | 33 | RTCDT2W682YF157M |
|  | 8200 | 90×130 | 0.15 | 41.1 | 20 | 30 | RTCDT2W822YF130M |
|  |  | 90×157 | 0.15 | 44.6 | 20 | 30 | RTCDT2W822YF157M |
|  | 10000 | 90×157 | 0.15 | 48.8 | 18 | 28 | RTCDT2W103YF157M |
|  |  | 90×170 | 0.15 | 48.8 | 18 | 28 | RTCDT2W103YF170M |
|  |  | 90×196 | 0.15 | 53.9 | 18 | 28 | RTCDT2W103YF196M |
|  | 12000 | 90×196 | 0.15 | 58.5 | 16 | 26 | RTCDT2W123YF196M |
|  |  | 90×236 | 0.15 | 63.8 | 16 | 26 | RTCDT2W123YF236M |
|  | 15000 | 77×235 | 0.15 | 53.7 | 14 | 24 | RTCDT2W153YE235M |
|  |  | 90×210 | 0.15 | 66.8 | 14 | 24 | RTCDT2W153YF210M |
|  |  | 90×236 | 0.15 | 68.9 | 14 | 24 | RTCDT2W153YF236M |
|  | 18000 | 101×250 | 0.15 | 80.6 | 12 | 22 | RTCDT2W183YG250M |
| 500 2H (550) | 1000 | 51×115 | 0.15 | 15.5 | 116 | 130 | RTCDT2H102YC115M |
|  | 1200 | 51×115 | 0.15 | 17.0 | 112 | 120 | RTCDT2H122YC115M |
|  | 1500 | 51×130 | 0.15 | 19.9 | 90 | 96 | RTCDT2H152YC130M |
|  | 1800 | 64×115 | 0.15 | 22.7 | 75 | 80 | RTCDT2H182YD115M |
|  | 2200 | 64×110 | 0.15 | 24.2 | 61 | 65 | RTCDT2H222YD110M |
|  |  | 64×130 | 0.15 | 26.1 | 61 | 65 | RTCDT2H222YD130M |
|  | 2700 | 77×115 | 0.15 | 29.0 | 50 | 53 | RTCDT2H272YE115M |
|  | 3300 | 77×130 | 0.15 | 33.7 | 45 | 48 | RTCDT2H332YE130M |
|  | 3900 | 77×155 | 0.15 | 39.2 | 38 | 41 | RTCDT2H392YE155M |
| Rated Voltage Code (V.DC) | Capacitance (μF) | Case size ΦD×L(mm) | tanδ 20℃, 120Hz | Ripple current 40℃, 120Hz (Arms) | ESR(typ.) 20℃, 100Hz (mΩ) | Z max 20℃, 10KHz (mΩ) | Part number |
| 500 2H (550) | 4700 | 77×170 | 0.15 | 44.9 | 34 | 37 | RTCDT2H472YE170M |
|  | 5600 | 77×195 | 0.15 | 51.6 | 28 | 31 | RTCDT2H562YE195M |
|  |  | 90×157 | 0.15 | 50.5 | 28 | 31 | RTCDT2H562YF157M |
|  | 6800 | 90×170 | 0.15 | 57.3 | 23 | 25 | RTCDT2H682YF170M |
|  | 8200 | 77×236 | 0.15 | 66.6 | 21 | 23 | RTCDT2H822YE236M |
|  |  | 90×196 | 0.15 | 66.4 | 21 | 23 | RTCDT2H822YF196M |
|  | 10000 | 90×236 | 0.15 | 69.5 | 17 | 19 | RTCDT2H103YF236M |
|  |  | 101×195 | 0.15 | 79.4 | 17 | 19 | RTCDT2H103YG195M |
|  | 12000 | 101×237 | 0.15 | 85.7 | 16 | 18 | RTCDT2H123YG237M |
|  | 18000 | 101×260 | 0.15 | 93.2 | 14 | 16 | RTCDT2H183YG260M |